## Slide 1: PHY1013S CIRCUITS
Gregor Leigh gregor.leigh@uct.ac.za

## Slide 2: DC CIRCUITS
Learning outcomes: At the end of this chapter you should be able to…
    Interpret and draw circuit diagrams.
    Use Kirchhoff’s laws to analyse circuits containing resistors (and capacitors), in series and in parallel.
    Measure resistance using the ammeter-voltmeter method and the null method involving a Wheatstone bridge.
    Relate emf and terminal potential difference through the internal resistance of cells and batteries.
    Perform calculations involving the growth and decay of current in RC circuits.

## Slide 3: KIRCHHOFF’S LAWS
Kirchhoff’s junction law:
  At any junction, the sum of the currents entering the junction equals the sum of the currents leaving:

## Slide 4: KIRCHHOFF’S LAWS
Kirchhoff’s junction law:
  At any junction, the sum of the currents entering the junction equals the sum of the currents leaving:
Kirchhoff’s loop law:
  In any closed path, the sum of all the potential differences encountered while moving around the loop is zero:

## Slide 5: RESISTORS IN SERIES
  When three resistors are connected in series, the current strength I is the same in all three.
  V1 = IR1, V2 = IR2, V3 = IR3, from which…
  V = V1 + V2 + V3 = I(R1 + R2 + R3)
  and hence the equivalent resistance Req , with the same applied potential difference and current strength, is
  In general, for any number of resistors in series:
V1
V2
V3
R1
I
V
V1
V2
V3
R2
R3
I
I
I

## Slide 6: RESISTORS IN PARALLEL
  In general, for any number of resistors in parallel:
  The total current strength through all three is the sum of the current strengths through the individual resistors:
  I = I1 + I2 + I3
  and since I = V/R …
  so
R1
R2
R3
I
I1
V
V
I2
V
I3
V

## Slide 7: MEASURING RESISTANCE
  If ideal ammeters (with no internal resistance) and ideal voltmeters (which drew no current) existed, it would be possible to measure resistance accurately using the voltmeter-ammeter method and .
  However…
  Real voltmeters and ammeters are simply modified galvanometers (micro-ammeters) and they do NOT behave ideally in all circumstances.
R
V
A

## Slide 8: MOVING COIL GALVANOMETER
N
scale
pointer
S
permanent
magnet
hair spring
soft-iron core
(moving) coil
N

## Slide 9: AMMETERS and VOLTMETERS
I
  In an ammeter, most of the current is made to bypass the galvanometer via a low resistance shunt :
  In a voltmeter, most of the current is prevented from passing through the galvanometer by a high resistance multiplier :
A
low R shunt
I
G
V
I
G
I
high R multiplier

## Slide 10: MEASURING RESISTANCE
  Determine the value of R,
  given that the voltmeter has an internal resistance of…
  RV = 2 k
   R = 6.02 
  RV = 50 
   R = 6.82 
R
V
A
2 A
12 V

## Slide 11: WHEATSTONE BRIDGE
  One or more of the three known resistances, R1, R2, or R3, are varied until there is no deflection on the sensitive galvanometer.
  Then, since VBD = 0,
  VAB = VAD and VBC = VDC
   I1R1 = I2R2 and I1R3 = I2Rx
R1
R2
R3
Rx
?
A
D
B
C
I1
I2
G

## Slide 12: EMF and INTERNAL RESISTANCE
  A voltmeter across a cell shows a lower reading when the cell is connected to a circuit. Why? What happens to these “lost volts”?
  Emf, E : The total amount of electrical energy supplied by a cell to a unit of charge. In other words, the potential difference across the cell when there is no current through it.
  Terminal pd: When current flows, the internal resistance, r, of the cell causes the charge to lose some energy (lost volts).

## Slide 13: EMF and INTERNAL RESISTANCE
  So the net voltage across the cell is lower than its emf. (Work needs to be done in the cell in order to drive the charge):
  IR = E – Ir
  i.e. terminal pd = emf – “lost volts”
  so internal resistance is added in series to R – when dealing with the emf of a cell :
  otherwise use only external resistance, R – when working with the terminal pd of the cell :

## Slide 14
A 12 V battery with an internal resistance of 0.5  is connected to a combination of resistors, as shown:
Determine the potential difference across:
  the terminals of the battery;
  X and Y.
X
Y
2 
1.6 
2 
4 
4 
4 
12 V r = 0.5 
12 
2.5 
Calculate the current in the bulb.
A battery consisting of two cells connected in parallel is connected to a 8  bulb. One of the cells has an emf of 1.5 V and an internal resistance of 0.2 , while the other is a 1.2 V cell with an internal resistance of 0.3 .
1.2 V 0.3 
1.5 V 0.2 
8 

## Slide 15
4 
  A 12 V battery with an internal resistance of 0.5  is connected to a combination of resistors, as shown:
12 V r = 0.5 
X
Y
12 
2 
1.6 
2 
2.5 
4 
4 
  Determine the potential difference across:
  the terminals of the battery;
  X and Y.
(a)
6 
2.4 
4 
2 
4 
3 
  terminal pd = E – Ir = 12 – (2)(0.5) = 11 V
  R + r = 6 
6 

## Slide 16
   VXY = 8 – 5 = 3 V
4 
  A 12 V battery with an internal resistance of 0.5  is connected to a combination of resistors, as shown:
12 V r = 0.5 
X
Y
12 
2 
1.6 
2 
2.5 
4 
4 
  Determine the potential difference across:
  the terminals of the battery;
  X and Y.
(b)
4 
  I2 = 12/16 Itotal = ¾ of 2 = 1.5 A
I
12/16 I
4/16 I
  V2 = I2 R2 = (1.5)(2) = 3 V
0 V
11 V
8 V
  V2.5 = I2.5 R2.5 = (2)(2.5) = 5 V
   VY = 5 V
   VX = 8 V
5 V

## Slide 17: KIRCHHOFF’S LOOP LAW
  Draw a labelled circuit diagram.
  In each loop, choose a current direction and indicate your choice with a labelled arrow.
  Move around each loop, adding voltages algebraically:
    moving through a battery from –ve to +ve, Vi = Vbat :
    moving through a battery from +ve to –ve, Vi = –Vbat :
    moving through a resistor, Vi = –InetR, where Inet is the net current in the direction you are moving.
  Apply the loop law to each loop.
  Problem-solving strategy:
I
I

## Slide 18
Calculate the current in the bulb.
A battery consisting of two cells connected in parallel is connected to a 8  bulb. One of the cells has an emf of 1.5 V and an internal resistance of 0.2 , while the other is a 1.2 V cell with an internal resistance of 0.3 .
1.2 V 0.3 
1.5 V 0.2 
8 
1. Draw a labelled circuit diagram.

## Slide 19
1.2 V 0.3 
1.5 V 0.2 
8 
Calculate the current in the bulb.
A battery consisting of two cells connected in parallel is connected to a 8  bulb. One of the cells has an emf of 1.5 V and an internal resistance of 0.2 , while the other is a 1.2 V cell with an internal resistance of 0.3 .
2. In each loop, choose a current direction and indicate your choice with a labelled arrow.
I1
I2

## Slide 20
1.2 V 0.3 
1.5 V 0.2 
8 
Calculate the current in the bulb.
A battery consisting of two cells connected in parallel is connected to a 8  bulb. One of the cells has an emf of 1.5 V and an internal resistance of 0.2 , while the other is a 1.2 V cell with an internal resistance of 0.3 .
3. Move around each loop, adding voltages algebraically.
(Inet is the net current in the direction you are moving.)
I1
I2
1.5
1.2
– 1.2
– 8.0 I2
– 0.3(I1 – I2)
– 0.3(I2 – I1) (2)
– 0.2 I1 (1)

## Slide 21
1.2 V 0.3 
1.5 V 0.2 
8 
= 0
= 0
Calculate the current in the bulb.
A battery consisting of two cells connected in parallel is connected to a 8  bulb. One of the cells has an emf of 1.5 V and an internal resistance of 0.2 , while the other is a 1.2 V cell with an internal resistance of 0.3 .
4. Apply the loop law to each loop.
I1
I2
1.2 + 0.3 I1 – 8.3 I2 = 0 (2)
0.3 – 0.5 I1 + 0.3 I2 = 0 (1)
(1)  3: 0.9 – 1.5 I1 + 0.9 I2 = 0 (3)
(2)  5: 6.0 + 1.5 I1 – 41.5 I2 = 0 (4)
(3) + (4): 6.9 – 40.6 I2 = 0
 I2 = 0.17 A
1.5
1.2
– 1.2
– 8.0 I2
– 0.3(I1 – I2)
– 0.3(I2 – I1)
– 0.2 I1

## Slide 22: RC CIRCUITS
  Applying Kirchhoff’s loop law:
  …where Q and I are the instantaneous values of the charge on the capacitor and the current through the resistor, and are related by
  In circuits containing both resistors and capacitors, current strength varies with time. I.e. RC circuits are time dependent.
  Hence
I
  (The product RC is a constant for any particular circuit.)
  and thus
+Q
–Q

## Slide 23: RC CIRCUITS
  Beginning at Q0, the value of the charge on the capacitor after time t is given by:
I
+Q
–Q

## Slide 24: RC CIRCUITS
  Taking exponents on both sides:
I
+Q
–Q
  and since this argument must be dimensionless, RC =  has dimensions of time, and is called the time constant of the circuit.
  Graphically:
  Q
  t
  0
  
  3
Q0
0.37Q0
0.13Q0
  2

## Slide 25: RC CIRCUITS
  Since it can also be shown that the resistor current varies similarly with time…
I
+Q
–Q
  I
  t
  0
  
  3
I0
0.37I0
0.13I0
  2
    The shape of the graphs is independent of ’s value.
    Theoretically, complete discharge occurs only after an infinite time, but after 5 there is practically no charge left (<1%).
  Notes:

## Slide 26: CHARGING A CAPACITOR
  While a capacitor is being charged, the charge on it increases according to:
  Hence:
  (What does the corresponding I vs t graph look like?)
  or
  And:
Qmax
  Q
  t
  0
  
  3
  2

## Slide 27
  The capacitors in the adjacent circuit are initially uncharged. Calculate:
12 
5 F
10 F
15 
15 
10 
S
50 V
  the initial battery current when switch S is closed;
  the steady-state battery current;
  the final charges on the capacitors.
(a)
  At switch-on the capacitors are “invisible” and the “square” becomes essentially just three parallel resistors:
I2
I1
I3

## Slide 28
S
  Rtot = (15 + 12 + 15) + 10 = 52 
  The capacitors in the adjacent circuit are initially uncharged. Calculate:
12 
5 F
10 F
15 
15 
10 
50 V
  the initial battery current when switch S is closed;
  the steady-state battery current;
  the final charges on the capacitors.
(b)
  Once the capacitors are fully charged they no longer “pass” current. The circuit is broken at these points and the only current path through the “square” is as shown.
I

## Slide 29
  The capacitors in the adjacent circuit are initially uncharged. Calculate:
12 
5 F
10 F
15 
15 
10 
50 V
  the initial battery current when switch S is closed;
  the steady-state battery current;
  the final charges on the capacitors.
(c)
I
  V10 = I10R10 = 0.96  10 = 9.6 V
50 V
40.4 V
40.4 V
0 V
0 V
  V15 = 0.96  15 = 14.4 V
  OR: V15+12 = 0.96  27 = 26 V
26 V
  Q10F = C10 F V10 F = 10–5  (40.4 – 14.4) = 260 C
14.4 V
  Q5F = 5  10–6  26 = 130 C