## Slide 1: The Audiogram
<number>
Measurement of Hearing and Audiogram Interpretation

## Slide 2: Introduction
<number>
How we measure hearing
How those measurements can be recorded
What the audiogram can tell us

## Slide 3: Purposes of audiometric testing
<number>
  Monitor the effectiveness of the hearing conservation program
  Identify significant threshold shift
  Establish readiness and fitness for duty
  Ensure proper referral and diagnosis

## Slide 4: Vocabulary
<number>
Audiogram - A record of a person’s pure-tone hearing threshold levels
Threshold – A level of sound that a person can detect 50% of the time or more
Audiometric Zero – sensitivity of normal, young adults

## Slide 5: Audiometric Zero (Ref ANSI S3.6 1996, TDH-39 earphones) 0 dB Hearing Level at 1000 Hz = 7 dB SPL
<number>

## Slide 6
<number>
Does 0 dB HL mean the absence of sound?
What is the intensity of a 0 dB HL pure-tone at 1000 Hz?

## Slide 7: Output Limits of the DOEHRS-HC Audiometer
<number>
-10 to 100 dB HL

## Slide 8: Serial Audiogram
<number>
Thresholds recorded to the nearest
5 dB
Used on DD Forms 2215 and 2216, entrance physicals and physical exam forms (SF 88 and DD 2808)

## Slide 9: Serial Audiogram
<number>

## Slide 10: Graphic Audiograms
<number>
Provides a pictorial representation of hearing thresholds as a function of frequency and intensity
Uses symbols and/or colors to represent right ear, left ear, bone conduction hearing and masking levels

## Slide 11: Graphic Audiograms
<number>

## Slide 12: Self-recording Audiogram
<number>

## Slide 13: Degrees of Hearing Loss
<number>
Normal Hearing -10 - 25 dB HL
Mild Hearing Loss 30 - 45 dB HL
Moderate Hearing Loss 50 - 65 dB HL
Severe Hearing Loss 70 - 85 dB HL
Profound Hearing Loss > 90 dB HL

## Slide 14: Audiogram Configurations: Progressive noise-induced hearing loss
<number>

## Slide 15: Hearing Loss Zones
<number>

## Slide 16
<number>
dB
Hz
250 500 1000 2000 3000 4000 6000 8000
sh
f
th
s
ch
p h
k
Speech Sounds

## Slide 17: Audiogram Configurations: Gundecking
<number>

## Slide 18: Audiogram Configurations: Background Noise
<number>

## Slide 19: Cross-over
<number>
One ear hears much better than the other
The sound presented to the test ear crosses through the skull and stimulates the hair cells of the cochlea of the non-test ear
The non-test ear is the one actually responding to the tone
Differences of > 40 dB at the same frequency between ears are suspicious

## Slide 20: Cross-over
<number>

## Slide 21: Malingering
<number>
Pretending to have a hearing loss by waiting until the sound is quite loud before pressing the response button
IAW Article 115, Paragraph 194, a person may be charged with malingering if he/she pretends to have a hearing loss that is later found to be non-existent

## Slide 22: Automatic Rechecks
<number>

## Slide 23: Sensorineural Hearing Loss
<number>
Determined by a complete audiological evaluation
Compare air-conduction and bone-conduction pure-tone thresholds
Look at acoustic immittance test results

## Slide 24: Sensorineural Hearing Loss
<number>

## Slide 25: Conductive Hearing Loss
<number>

## Slide 26: Counseling Patients
<number>

## Slide 27: Explain the Test Results
<number>
Provide privacy for explanation
Both ears tested
Frequencies tested
The lower the threshold, the better the hearing
Review each ear in terms of intensity and frequency

## Slide 28: Appropriate Explanations
<number>
Within normal limits
Loss in the high or low frequencies
Loss in one or both ears
Hearing has changed or remained the same

## Slide 29: Making Diagnoses
<number>

## Slide 30
<number>
Medical Legal Requirements Regardless of Type
Patient’s name, SSN, (MOS, SSI, Job Location, and Unit Identification Code)
Examiner’s name, SSN, and certification number
Date of Test
Make, model, and serial number of audiometer
Calibration date of audiometer.
Notes: <number>

## Slide 31
<number>
DOEHRS-HC supplies most of the necessary medical legal audiogram information AUTOMATICALLY

## Slide 32: DD Form 2215 Reference Audiogram
<number>
For all military and noise-exposed civilians
Performed before noise-hazardous duties or as soon as possible thereafter
Noise-free period of at least 14 hours before the test
No temporary ENT problems the day of test
Refer for low-frequency or high-frequency hearing loss
After a permanent STS, re-establish a new baseline

## Slide 33: DD Form 2216 Hearing Conservation Data
<number>
Periodic audiogram
Annual
90 - Day
Termination
Other

## Slide 34: Forms General Information
<number>
Maintain audiograms for entire period of employment plus 5 years
Test must be performed by audiologist, physician, persons certified by CAOHC, or one who has received equivalent military training
Equivalent military training includes this course. The certification from this course and other Army courses is only 5 years

## Slide 35: Audiogram Review
<number>
Trained personnel must review all audiograms for validity and proper patient disposition.
  Who Reviews?
  Initially any Hearing Conservation Technician
  Problem audiograms must be reviewed by an audiologist, otolaryngologist or other physician
Notes: <number>

## Slide 36: Audiograms to Refer
<number>
DD 2215’s
  > 25 dB at 500, 1000, and 2000 Hz
  > 55 dB at 3000, 4000, or 6000 Hz
DD 2216’s
  Significant Threshold Shift (STS) computed from the average of 2000, 3000, & 4000 Hz in either ear in comparison to the baseline or reference hearing test (DD2215)

## Slide 37: Factors Affecting Validity
<number>
Poor test environment - audiometric test booth does not meet background noise criteria
Cross-over hearing
Uncooperative patients

## Slide 38: Review Questions
<number>
Does an audiometric booth need to be perfectly soundproof?
Excessive noise in an audiometric test booth will probably effect which frequency?
When hearing levels between ears at the same frequency differ by 50 to 70 dB, what should you suspect is going on?